## Slide 1: Nyra MES — Activated Carbon Process Flow
1-month trial for GR Carbons
Supplier inward → production lot → shop floor → finished goods → dispatch

## Slide 2: Scope of the trial
Raw material: inward receipt, QC, release to production (PO + LOT)
Production gate: feasibility, kiln feed, lot routing
Shop-floor execution with step-wise data capture
Finished-goods in stock and customer dispatch
Dashboard, traceability, kiln parameters & telemetry (as enabled)

## Slide 3: End-to-end flow (bird's eye view)
SUPPLIER INWARD → RAW MATERIAL QC → RELEASE TO PRODUCTION
↓
FEASIBILITY GATE → KILN FEED → LOT ROUTING → EXECUTION
↓
FINISHED GOODS IN STOCK → DISPATCH
Inward order: ORD-AC-* · Production lot: LOT-AC-* · Work orders from routing
After release, operators and planners work on LOT codes, not inward orders.

## Slide 4: Phase 1 — Raw material (3 screens)
1. Inward — supplier, raw material type, quantity received (KG)
2. Raw material QC — lab/yard tests; Pass / Fail / Hold
3. Release to production — allocate KG; creates production order + LOT-AC-*
Release may create one lot or multiple lots (one per bag grade when grade splits exist).
All weights in KG unless noted as % on QC forms.

## Slide 5: Data captured — raw material
Inward
Supplier
Raw material type
Quantity received (KG)
Optional / extensible: DC number, supplier weight (KG), value (INR)
Raw material QC (configurable)
Moisture, ash, foreign matter (%)
Stones, unburnt, -20 mesh fines (KG)
QC status & operator remarks
Stored on inward order; feasibility checks QC passed

## Slide 6: Optional inbound depth (platform capability)
Same inward order can also store: initial QC (moisture, dust, AD)
Bag split & reconcile → weight to crusher
Crusher: rotary A/B; mesh scrap +2 … -14 (KG); moisture & dust (%)
Six bag-grade splits → mass balance & multi-lot release
Primary trial UI: Inward + QC + Release — extended steps aligned with GR SOP in workshop

## Slide 7: Inbound — triplet ontology (order-scoped)
Subject: urn:nyra:ac:inward:{ORD-AC-code} (before release)
Inward receipt — supplies / captures: DC, supplier weight, received KG, value INR
Initial QC — testedBy → initialQc; moisture, dust, AD parameters
Bags — containedIn; crusher & grade separation — captures mesh scrap & grade KG
Raw Material QC tab — testedBy → rawMaterialQc; stones / unburnt / -20 KG predicates

## Slide 8: Phase 2 — Production gate
Feasibility Gate — select LOT-AC-*; checks material (QC), kiln availability, resources
Kiln Feed — charge activation kiln; lot IN_PROGRESS
Lot Routing — generate work orders from raw-material routing template (Masters)
Routing defines pyrolysis, activation, screening, grade separation, FG QC, etc.

## Slide 9: Triplet ontology — what it is
Semantic trace layer: kg.triple_store_staging (PostgreSQL) + MES operational tables
Each save can stage subject · predicate · object (+ literal parameters)
Inward steps use subject: urn:nyra:ac:inward:{ORD-AC-*}
After release, production & execution use: urn:nyra:ac:lot:{LOT-AC-*}
Same data operators enter in UI — triples enable traceability, analytics, Ask Nyra

## Slide 10: Phase 3 — Shop-floor execution (operational data)
Every routing step (Execution screen)
Start · Complete · Hold on each work order
Actual output (KG) · Scrap (KG) · Downtime (min)
Operator / labor pool · Machine when required
Routing parameters (temps, steam, time, …) on complete
Stored: exec.operation_execution + parameter readings
Dedicated step panels (Execution)
SCREENING — mesh; good / overs / fines (KG)
GRADE_SEPARATION — grade code; separated KG; yield
QC — iodine, ash, moisture, bulk density; disposition
Release to in-stock moves lot to FG stock when pipeline complete

## Slide 11: Execution — triplet ontology (lot-scoped)
Subject for all rows below: urn:nyra:ac:lot:{LOT-AC-code}
SCREENING (on save in Execution)
• screenedAt → urn:nyra:ac:screening:{execution_code}
• captures: SCREEN_MESH_SIZE, GOOD_KG, OVERS_KG, FINES_KG
GRADE SEPARATION (on save in Execution)
• captures → urn:nyra:ac:gradeSeparation:{execution_code}
• captures: GRADE_CODE, SEPARATED_KG, GRADE_YIELD_PCT, OVERS_GRADE_KG, FINES_GRADE_KG

## Slide 12: Execution — triplet ontology (continued)
QUALITY TESTING (on save — Release to in-stock)
• testedBy → urn:nyra:ac:qualityCheck:{QC-AC-code} (ontology)
• Lab values in qms.quality_check metadata (iodine, ash, moisture, bulk density)
• hasIodineValue staged on lot when iodine entered
DISPATCH (when shipping)
• dispatchedTo — lot linked to customer shipment
Pyrolysis / activation / kiln hourly params: operational executions + lot metadata
(extend triple parameters in trial where GR needs explicit KG predicates)

## Slide 13: Pre-execution triples (same lot subject)
Feasibility Gate — feasibilityChecked → urn:nyra:ac:feasibility:{lot}
Kiln Feed — assignedTo → urn:nyra:ac:kiln:{kiln_resource_code}
Lot Routing — generates → urn:nyra:ac:routing:{lot}
Links planner actions to the same LOT-AC-* trace chain as Execution

## Slide 14: Phase 4 — Stock & dispatch
Release to in-stock — when routing complete, screening recorded, QC passed
Lot status & FG stock updated — visible on Dispatch
Customer PO — order against finished product; stock check
Dispatch — ship from in-stock by grade; traceability ORD → LOT → QC → dispatch

## Slide 15: Supporting capabilities
Operational Intelligence Hub — KPIs, pipeline, kiln strip
Kiln parameters — hourly / zone readings per lot
Kiln telemetry — live Modbus path (testbed)
Masters — suppliers, materials, kilns, routing template, QC/quality fields
Reports, traceability, bag tracing (capabilities per tenant)

## Slide 16: Configured for GR Carbons
Raw material types and fixed routing per feedstock
QC & finished-goods quality fields (Masters → Ontology)
Plant resources — kilns, labor pools, tools
Grade names & mesh bands — workshop with GR during trial
Trial validates your SOP against this model, not a generic demo only

## Slide 17: Trial access
URL: https://nyraservices-testbed.net/mes/
Module: Activated Carbon · secure login (GR tenant / workspace)
Architecture: PostgreSQL nyra_mes_core, REST API, audit trail
Suggested pilot: one inward → QC → release → one lot through feasibility, kiln, routing, execution, in-stock

## Slide 18: Workshop — what else should we capture?
Mandatory inward fields (DC, weighbridge, commercial value)?
Crusher / bag / mesh scrap on every receipt — UI priority?
Actual routing steps vs plant (kiln → activation → screening → QC)?
Mandatory lab tests on raw vs finished carbon?
COA, certificates, photos? PLC / weighbridge / LIMS later?

## Slide 19: Summary
One chain: Supplier → QC → Lot → Kiln → Execute → Stock → Dispatch
Lot-centric after release (LOT-AC-*)
Operational data + triplet ontology on key execution steps (screening, grades, QC)
Configurable for GR Carbons grades, tests, and routing
Next: joint testbed walkthrough + configuration workshop