## Slide 1
GR CARBONS · NYRA MES
Activated Carbon Process Flow
From supplier inward to kiln, post-activation, customer PO and dispatch. Working copy — edit freely before the meeting.

## Slide 2
Agenda
What we will walk through
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• How the plant is modelled in Nyra MES
• End-to-end material flow (one picture)
• Raw Material — gate, lab, RMS, crusher, release
• Execution — Activation (kiln) then Post-activation
• Customer PO, In Stock, and Dispatch
• Who uses which screens (Admin vs shop floor)

## Slide 3
How the application is organised
Left menu in Nyra MES — Activated Carbon
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Overview
• Dashboard
• Kiln telemetry
Production
• Raw Material
• Execution
• Customer PO
• Dispatch
• Reports
Admin
• Users
• Customer
• Supplier
Masters
• Materials & steps
• Machines & kilns
• Routing
• Inbound settings

## Slide 4
End-to-end plant flow
One chain — from the gate to the customer
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Gate
receipt
Inbound
prep
Release to
production
Kiln
activation
Post-
activation
In Stock &
Dispatch
Shop identity
Plant users work with the inward order ORD-AC-* until release. They think in bags (RI / RO / KA / DS), not internal lot numbers.
After release
Execution starts at kiln feed. Load on Kiln A or Kiln B. Remaining activation and post-activation steps are tabs on Execution.
Stock to ship
Bags marked In Stock after destoning or post-activation become available on Customer PO and Dispatch.

## Slide 5
Who uses which screens
Plant roles — keep this slide if you want to assign logins in the meeting
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Admin
Users, Customer, Supplier. Dashboard only besides Admin.
RMS
Raw Material — gate, lab, bags, crusher, outward, release.
Activation
Execution — kiln feed, kiln output, destoning, kiln parameters.
Post Activation
Execution — screening through finished goods.
Quality
Quality tabs on kiln feed, kiln output, destoning, post-activation.
Manager
Plant screens plus Customer PO, Dispatch, Reports.
nyraservices
Everything, including Masters and Routing Builder.

## Slide 6
Raw Material — four tabs
Screen: Raw Material
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
1 · Gate receipt
Supplier inward at the dock. DC number, supplier kg, our kg.
2 · Inbound prep
Lab → RMS inward → Crusher → RMS outward.
3 · Release
Release the inward order to production. Then go to Execution.
4 · Reports
Read-only. Process dropdown, charts, Excel. No capture.

## Slide 7
Gate receipt
First capture — identity of the inward is ORD-AC-*
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Supplier (from Admin → Supplier)
• Raw material type (Coconut Shell)
• DC number — required
• Supplier weight (KG) — required
• Our weight (KG) — this is received quantity
• System creates the inward order ORD-AC-*
• A production order and lot are created in the background for trace — not shown to the operator
Operator sees
ORD-AC-1
Not PO-AC-*
Not LOT-AC-*
“Lot” on the floor =
RMS outward bags

## Slide 8
Inbound prep — four steps after the gate
Must be completed in this order on the same inward
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
1. Lab
IN-LAB
Moisture %, dust %, AD. Approve or Deny. Deny needs remarks and stops this inward only.
2. RMS inward
IN-RMS-BAG
Bags RI_BAG_001… Total bag KG must equal our weight from the gate.
3. Crusher
IN-CRUSHER
Feed RMS bags one by one. Grade, dust %, moisture %, rotary.
4. RMS outward
IN-RM-OUT
Output bags RO_BAG_001… Rotary A or B. Grade + Unburnt + Stones.

## Slide 9
RMS outward — rotary grades
Configured in Masters → Inbound settings (nyraservices)
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Choose Rotary A or Rotary B for crusher output bags
• That rotary needs a grade value, plus Unburnt and Stones
• Rotary A typically: -20 1st Stage, Grade 1st stage
• Rotary B typically: -20 2nd Stage, Grade 2nd stage
• Kiln feed loads only rotary grades — Unburnt and Stones stay off the kiln
• Release shows the RO_BAG_* details from this step

## Slide 10
Release to production
Raw Material tab 3 — then Execution
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Completing RMS outward auto-marks the inward so release can proceed (no separate RM QC screen)
• Release allocates charcoal to production
• Operator then opens Execution — kiln feed is first
• Feasibility gate is not used on the floor (it redirects to Execution)
• Lot routing is not a separate screen — Load on the kiln creates the work tabs

## Slide 11
Execution — Activation
Sidebar: Execution → Activation
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Kiln feed
Load RO_BAG_* onto Kiln A or Kiln B. Live load graph. Quality on feed bags.
Kiln output
Output bags KA_DDMMYY_##### or KB_DDMMYY_#####. Output quality.
Destoning
Creates DS_DDMMYY_#####. Destination can be In Stock.
Kiln parameters
Hourly readings with timestamp. Not lot-specific — a plant reading.
Reports
Read-only activation report. Process flow pane is hidden.

## Slide 12
Execution — Post-activation
Sidebar: Execution → Post activation
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Screening
SC_
De-dusting
DD_
Crushing
CR_
De-mag
DM_
Blending
BL_
Finished
goods FG_
• Each station has live load and output bags dated DDMMYY
• De-dusting and de-magnetisation output grade is Exklin only
• Destination In Stock makes those bags available for Customer PO
• Quality tab on post-activation; Reports tab is read-only
• Process flow stays on the right pane — it is removed when Reports is open

## Slide 13
Numbers the plant will see
Each key has its own PostgreSQL sequence
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
ORD-AC-*
Inward / shop identity
RI_BAG_*
RMS inward bags
RO_BAG_*
RMS outward bags
KA_ / KB_
Kiln A / Kiln B output
DS_*
Destoning bags
SC_ DD_ CR_
DM_ BL_ FG_
Post-activation bags
CUST_PO_*
Customer sales PO
DISP-AC-*
Dispatch document

## Slide 14
Customer PO and Dispatch
Finished carbon leaving the plant
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Customer PO
Dispatch
• Create CUST_PO_* against a customer
• Available stock = destoning / post-activation bags with destination In Stock
• Not leftover FG metadata
• Ship against a customer PO — shown at the top
• Pick In Stock bags (or oldest first)
• Dispatch identity DISP-AC-*

## Slide 15
Dashboard and Reports
Management view vs shop-floor capture
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Dashboard tabs: Overview, Raw Material, Activation, Post-activation, Machine utilization
• High-level KPIs: charcoal at dock, GC, plant yield, kiln yield, Exklin with / without stone
• Machine counts come from Masters → Machines & kilns
• Section Reports (RM / Activation / Post-activation) are read-only — charts and Excel
• Reports do not write shop-floor data and do not change the process flow

## Slide 16
Admin vs Masters
Who is allowed to change plant setup
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
Admin — plant administrator
Masters — nyraservices only
• Users (create plant logins)
• Customer (who you sell to)
• Supplier (who delivers charcoal)
• Materials & process steps
• Machines, kilns, routing
• Kiln reading fields
• Inbound rotary settings

## Slide 17
Shop-floor rules worth stating in the meeting
These are live in the application today
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Weights are KG. Moisture and dust are %. AD is a lab reading, not a weight
• RMS inward bags have no grade; outward bags carry the rotary split as grade
• Lab deny stops that inward only — other inwards continue
• Do not click capture buttons twice; the screen stays locked until the save finishes
• Process flow is on the right of Execution; it is hidden on Reports

## Slide 18
Suggested live walkthrough
One receipt through to a dispatch
Nyra MES · GR Carbons Activated Carbon · Process flow · Editable working copy
• Admin: confirm supplier and customer exist
• Raw Material: gate receipt → lab approve → RMS bags → crusher → RMS outward
• Release to production
• Execution Activation: load kiln → output bags → destoning (optional In Stock)
• Execution Post-activation: screening → … → finished goods / In Stock
• Customer PO against In Stock → Dispatch against that PO
• Dashboard / Reports to show the same kg in management view

## Slide 19
One chain. One plant.
Supplier inward → kiln → post-activation → In Stock → customer. Nyra MES keeps the shop-floor capture and the trace together.